## Slide 1: Launch Relay System - Design
Wireless fill and launch control
  N2O fill/vent, O2 fill, quick disconnect, igniter
  Wired data connection to rocket
Modularity and future SRT use
  Solenoid compatibility
    Hold o/c, pulse o/c, 12 VDC, 24 VDC
  1 or 2 car battery operation
  3 extra channels (easily expandable)
Safety
  Separate computer power source
  Pushbutton 20 mA igniter continuity test
  Primary arming key switch and igniter disable switch
  Remote control solenoid and igniter arming (with buzzer)
Launch Control
Electronics and Payload
3 Types of Solenoids

## Slide 2: Launch Relay System – Key Components
Container and interface
  ABS hinged box
  15" L x 11" W x 6” H
  Steel mounting plate
  Stainless DIN 3 rail
  12x 20 A receptacles for solenoids
  4x car battery clamps
Switching and control
  Arduino Mega 2560 R3
  16x N-channel MOSFETs
  11x SPDT 16 A relays
  2x arming relays
  100 A igniter relay
Launch Control
Electronics and Payload
Launch Box Interface Panel

## Slide 3: Launch Relay System - Diagram
Launch Control
Electronics and Payload
Arduino Mega
9V Battery
(Arduino ~5 hr
supply)
5 pack N-Ch
MOSFETs
12 V Car
Battery
Arming Key
Switch and Relay
16 A Solenoid Relays
(built in flyback diode
and test LED)
24 V Relay
Section
Warning
Buzzer
24 V Step-Up
(Car Battery)
Continuity Test
Igniter Relay and
Lockout Switch
Igniter Arming
MOSFET (-)

## Slide 4: Launch Relay System – Sequence
Connect batteries
Power on computer
Power on solenoids
Test igniter continuity
Enable igniter circuit
Arm with the key switch
Move personnel to safe distance
Wirelessly activate arming relay (buzzer sounds)
Oxidizer fill sequence
Wirelessly arm igniter relay
Ignition
Disarm in reverse
Launch Control
Electronics and Payload
Launch Box Interface Panel
2.
3.
4.
5.
6.
8.