## Slide 1
Electronics and Payload

## Slide 2: E&P Team Overview
Objective: Develop and test all electronic systems to support the team. Integrate a unique and competitive 10 pound payload.
Progress:
Reselected primary flight computer
Finished design of E&P bay, launch control system, sensor package
Began prototyping, construction and parts ordering
Payload collaboration/integration
Finished (mostly) Riverside engine test facility
Overview
Electronics & Payload

## Slide 3: Engine Test Facility
Engine Test Stand
Redesigned/rebuilt from ground up
Completely integrated electrical system
  Capable of supporting variety of sensors and controls
Electronics & Payload

## Slide 4: Engine Test Facility
Engine Test Stand
Electronics & Payload
Streamlined engine testing process
  Camera feed, live data/control from inside nearby building
  Permanently installed DAQ, control circuitry, lighting, etc.
  Gas cylinder storage area
  Underground power line (401 class; in progress)
  Remaining parts/supplies to be ordered then installed (1-2 days work)

## Slide 6: Electronics Overview
Electronics will consist of two similar and connected, but functionally separate bays.
The avionics bay, housing mission critical electronics
The payload bay which doubles as support for the satellites as well as providing extra weight
Payload bay connected to avionics bay below using bolts
Entire system integrated with rockets using U bolts below nose cone
E&P Bay
Electronics & Payload

## Slide 7: Payload
Rules:
  Must be a minimum of ten lbs
  Must be of scientific/engineering merit
  Cannot interfere with rocket stabilization
CubeSat Payload:
  Two teams each developed a 1U cube satellite, based at University of Sydney led by Dr. Xiaofeng Wu
  We will be collaborating to “field test” their design, see how it preforms under launch conditions, visiting in the coming months
  Bonus creativity and points for international effort on extremely valid engineering payload
  Both satellites expected to be around 2.2 lbs. a piece, coming to around 4.5 lbs total
  To make up for this weight deficiency, we are creating a payload bay which will house the two satellites as well as provide additional weight.
Payload
Electronics & Payload

## Slide 8: Satellite Bay
Design
  Connected to avionics bay at the bottom, creating a full tower
  The satellite bay will be two milled pieces of aluminum in place of wood slats to increase weight
  Placed horizontally and connected by three all thread bolts and lock nuts like avionics bay
  Each satellite placed on a aluminum slat in separate “story”
  At free hanging end, we will have padding placed at bottom of chamber to lend lateral direction support during launch jostling
Payload
Electronics & Payload

## Slide 9: Avionics Mounting
Requirements/Rules
  Our goal is to provide a separate and detachable electronics tower, capable of accepting various sensors at different locations, while adhering to competition rules
Design
  Avionics tower will be machined out of hard plywood
  Three horizontal platforms, creating two sections, bottom for battery, top for primary electronics, holes drilled through platforms for wires
  Top section has vertical board for all electronics to be mounted on for single axis mindfulness
  Two additional bottom section mounts for additional surface
  Three all thread rods, secured with lock nuts at each platform, going all the way through
  Connected to rocket body using recovery bulkhead U bolts at top
Electronics Bay
Electronics & Payload

## Slide 10: Launch Relay System - Design
Wireless fill and launch control
  N2O fill/vent, O2 fill, quick disconnect, igniter
Modularity and future SRT use
  Solenoid compatibility
    Hold o/c, pulse o/c, 12 VDC, 24 VDC
  1 or 2 car battery operation
  3 extra channels (easily expandable)
Safety
  Separate computer power source
  Pushbutton 20 mA igniter continuity test
  Primary arming key switch and igniter disable switch
  Remote control solenoid and igniter arming (with buzzer)
Launch Control
3 Types of Solenoids
Electronics & Payload

## Slide 11: Launch Relay System – Key Components
Container and interface
  ABS hinged box
  15" L x 11" W x 6” H
  Steel mounting plate
  Stainless DIN 3 rail
  Identical Riverside receptacles
  4x car battery clamps
Switching and control
  Arduino Mega 2560 R3
  16x N-channel MOSFETs
  11x SPDT 16 A relays
  2x arming relays
  100 A igniter relay
Launch Control
Launch Box Interface Panel
Electronics & Payload

## Slide 12: Launch Relay System - Diagram
Launch Control
Arduino Mega
9V Battery
(Arduino ~5 hr
supply)
5 pack N-Ch
MOSFETs
12 V Car
Battery
Arming Key
Switch and Relay
16 A Solenoid Relays
(built in flyback diode
and test LED)
24 V Relay
Section
Warning
Buzzer
24 V Step-Up
(Car Battery)
Continuity Test
Igniter Relay and
Lockout Switch
Igniter Arming
MOSFET (-)
Electronics & Payload

## Slide 13: Data & Communication Systems Architecture
Wireless Comm.
Electronics & Payload

## Slide 14: Data Transmission
Wireless Comm.
Use launch operations computer to send command to launch box
MathWorks includes support package for Arduino communication
Arduino receives command then sends back that it received command
If Arduino does not acknowledge, we will know to send command again
Arduino sends status update when command is completed
In case of sensors, data collection begins
In case of one-time command, a short message is sent
One wireless 900 MHz channel between launch box and launch operations computer
Electronics & Payload

## Slide 15: Sensors
Necessary for testing and flight data collection
  Vehicle will contain an IMU, two pressure sensors, and three thermocouples
Data will be read in and processed by Arduino Pro Minis
  System very flexible
    Allows for additional sensor or microcontrollers
  Data stored in 32 GB microSD cards
Flight Sensors
Electronics & Payload

## Slide 16: Rocket Safety System
Course deviation failure prevention system
  IMU data continually processed to determine if shutdown is appropriate based on vehicle orientation
In event of shutdown, oxidizer’s ball valve is closed and the venting needle valve is opened.
Rocket Safety
Electronics & Payload
Notes: Data in sensors is inherently “jumpy” so multi-data-point average necessary for useful data
  Thorough testing of IMU necessary to test for drift
Speed of ball valve closure greatly determines effectiveness of such measures

## Slide 17: Power Requirements
Power
Will be utilizing last year’s battery
Arduinos require much less power than BeagleBones so have plenty of energy to spare with last years battery
  This means any additional sensors added do not cause a concern with regard to power
Sensor | Voltage Draw | Current Draw (ea) | Power Draw (ea) | Quantity
Thermocouple | 3.3 V | Negligible | N/A | 3
IMU | 3.3 V | 1.2 mA | 3.96 mW | 1
Strain Gauge | 5 V | 100 mA | 500 mW | 2
Pressure Transducer | 12 V | 10 mA | 120 mW | 2
Arduino Pro Mini | 5 V | 25 mA | 125 mW | 3
Flight Total: | - | 296.2.2 mA | 1.619 W | 11
Electronics & Payload
Notes: Arduinos are able to output 500 mA each

## Slide 18: Data Transmission- Antennas
Home built Yagi antennas to gain experience while lowering cost
Prototype currently under construction, commercial antennas will be purchased if prototype proves ineffective
Element spacing and geometry calculated using antenna construction calculator
  Driven Element: Folded dipole copper tube, folded by 3D printed tube bender
  Frequency: 900 Mhz
  Directors: 5
  Wavelength: 333 mm
  Coax: 50 Ohm
  Directors/Reflector: Aluminum tube
  Insulated wooden boom
  Elevation: 7+ feet
Wireless comm.
Electronics & Payload

## Slide 19: Critical Flight Operations - Recovery
Flight Computers
StratoLogger CF Redundant Flight Computer
2 pyro channels
18 minute recording time
One 9V standalone battery
20 samples per second
Reused from SRT-2
Stratologger CF
TeleMega Primary Flight Computer
Highly recommended
3.7V LiPo battery as required by manufacturer
Additional 9V pyro battery
6 pyro channels
Newly purchased component - 33% discount
Will not be using telemetry, basis for future teams
TeleMega
Electronics & Payload

## Slide 20: Critical Flight Operations – Tracking & Recovery
Beeline GPS
Frequency: 430 MHz
10 mile LOS range
Secured inside fiberglass nosecone
5 second data packet intervals
Standalone system from electronics bay
Received using elevated commercial antenna
Packets decoded with mobile phone app
Reused from SRT-2
Upcoming range test with level 2 rocket
Tracking
Electronics & Payload
Beeline GPS 17

## Slide 21: Assembly Process
Entire E&P bay assembled outside of body tube, including battery connections
Toggle switches keep all components powered off
  Each flight computer has a separate dedicated switch
  DPDT, switching power from the 9V batteries and the built-in switch terminals
  All other components under single switch from 12 V battery
Entire E&P bay put into body tube (components off)
After rocket is ready for flight, switches flipped through pressure port holes
  Static pressure port area found using rocketry rule of thumb: ¼ inch hole per 100 inch3 , ~4 ½” holes
Assembly
Electronics & Payload